## Slide 1: RF Technology
By.Prateek Singh
Date:13/05/2025
Under the Guidance of : Dr. D. G. Bhalke
Dr. D. Y. Patil Institute of Technology
Notes: (Blue)
Paul G. Allen School of Computer Science and Engineering, UW

## Slide 2: Motivation Design Hardware Implementation Results Conclusion References Challenges & Future Work
Notes: (Blue)

## Slide 3: Motivation: Ubiquitous Connectivity
Implementing communication between billions of devices
Requirements
  Reliable and long range communication
  Low power
  Inexpensive to manufacture
Issues
  No existing technology combines all three factors
  E.g., backscattering is low power and cheap, but short ranged
Solution
  LoRa

## Slide 4: Applications
Smart cities
Precision agriculture
Whole-home and office sensing
Body-mounted medical sensing
Images courtesy of longrange.cs.washington.edu

## Slide 5: Motivation Design Hardware Implementation Results Conclusion References Challenges & Future Work

## Slide 6: Why LoRa ?
Advantages:
Low power consumption (three orders of magnitude lower than radios; not significantly better than other backscatter modes)
High operating range (100s of meters compared to tens for other backscatter modes)
Low cost and size (primarily digital construction materials)
Alternatives Explored:
Radios
Wi-Fi
BLE
ZigBee
SigFox
Backscatter
RFID
Passive Wi-Fi
Notes: (Blue)

## Slide 7: RF Module
RF zigbee Module
RF NRF Module
Low Power Consumption.
Easy For RF-based Application.
Complete Radio Transmitter.
Transmit Range Up To 50m.
CMOS / TTL Input.
Integrated, Wire Antenna
Interoperable other ZigBee-compliant devices
15 general-purpose I/O lines
Industry-leading sleep current of sub 1 µA
Transmit Range Up To 1km.
Voltage: 3-3.6V (recommended 3.3V).
Maximum output power: +20dBm.
Power-down mode current: 4.2uA.
Operating Range: 1Km
Receive Mode Current(peak): 45mA
It uses 2.4GHz global open ISM band.
Notes: (Blue)

## Slide 8: Why LoRa ?
Notes: (Blue)

## Slide 9: LoRa Architecture
The LoRa wireless uses a chirp-spread spectrum (CSS) modulation with options for different Spreading Factors (SF) and bandwidth to optimize the modulation to meet the range and data requirements.
LoRa uses ISM bands 433MHz, 868MHz or 915MHz depending on jurisdiction with the band divided up into channels.
LoRa network consists of several elements. Most of the modern LoRa IoT LAN technologies use mesh network architecture.
  LoRa Nodes/ End points
  LoRa Gateways
  Network servers
  Application server
Notes: (Blue)

## Slide 10: Synthesizing CSS with Backscatter
Recall: Chirp spread spectrum (CSS) encodes data as cyclic time shifts of the baseline “chirp,” which appear as frequency shifts after an FFT.
Notes: (Blue)

## Slide 11: Synthesizing CSS with Backscatter
Recall: Chirp spread spectrum (CSS) encodes data as cyclic time shifts of the baseline “chirp,” which appear as frequency shifts after an FFT.
Bit rate: BW/(2SF)•SF (BW = bandwidth; SF = spreading factor)
Notes: (Blue)

## Slide 12: Backscatter Harmonic Cancellation
Issues in signal approximation with square waves
  Creates mirror copies at third and fifth harmonics
  Prior systems ignored these signals (out-of-band)
  Noisy for LoRa due to high sensitivity
Solution
  Use different signal than a square wave
  Square waves have two voltage levels → high frequency components
  Multilevel signal to better approximate sinusoid
  Designed such that third and fifth harmonics are cancelled

## Slide 13: Reverse-Engineering LoRa Packet Structure
Challenge: physical layer specification for LoRa is proprietary
Solution:
  Reverse-engineer LoRa physical layer using Semtech patents
  Analyze transmissions from LoRa chipsets on a Universal Software Radio Peripheral (USRP)
Notes: (Blue)

## Slide 14: Reverse-Engineering LoRa Packet Structure
Challenge: physical layer specification for LoRa is proprietary
Solution:
  Reverse-engineer LoRa physical layer using Semtech patents
  Analyze transmissions from LoRa chipsets on a Universal Software Radio Peripheral (USRP)
Notes: (Blue)
CRC = cyclic redundancy check (an error-detecting code)

## Slide 15: Setting LoRa Parameters
LoRa bit rate determined by 3 factors:
  chirp bandwidth
  spreading factor
  error correction coding rate
BW and SF set in advance, known by transmitter & receiver
High sensitivity: phase of chirps must change continuously with time and have same value at each end of chirp
  At each frequency, increase phase by 2𝜋/SF
To comply with FCC, frequency-hop the single-tone chirp transmitter
  Backscatter device continues to be offset by Δf
Notes: (Blue)

## Slide 16: Motivation Design Hardware Implementation Results Conclusion References Challenges & Future Work

## Slide 17: Hardware Implementation

## Slide 18: Hardware Implementation
Digital Baseband Processor sends the spreading factor (SF) to the DAC to be converted to an analog voltage
The DAC’s output controls the oscillation speed of the VCO
VCO’s output is mapped to used to select appropriate impedance

## Slide 19: Hardware Implementation
Designed custom IC to minimize costs
Consists of three main components
Baseband Processor
  Creates LoRa packet using SF, BW, and code rate
  Sends packet data to Frequency Synthesizer to create the CSS signal
  Uses 1.25𝜇W to make packet with SF=12, BW=3.25kHz, and an (8, 4) Hamming code

## Slide 20: Hardware Implementation
Uses an extremely small amount of power
  Other systems use complex analog components
  Backscatter systems use switches to modulate reflections
Costs extremely cheap
  IC costs proportional to size of chip
  Active radio devices like for Wi-Fi, LoRa, BLE have about 10mm2 die area used for RF components
  Backscatter systems like RFID use about 0.15mm2 of die area
  This LoRa backscatter system uses <0.01mm2 of die area
    Switches use space efficient resistors and capacitors
    Metal in metal capacitors made on metal layers on top of MOS structures
Notes: Cheap because efficient use of space

## Slide 21: Motivation Design Hardware Implementation Results Conclusion References Challenges & Future Work

## Slide 22: Results Overview
Receiver Characterization
Operational Range
Wide-Area Applications
  Whole-Home and Office Sensing
RF-Challenged Applications
  Smart Contact Lens
  Flexible Epidermal Patch Sensor
Notes: (Blue)

## Slide 23: Receiver Characterization
Wired setup (avoid multipath complications)
Semtech SX1276 chipsets are both CSS transmitter and receiver
Conclusion: sensitivity is inversely proportional to the data rate of the packet
  Below -142 dBm, receiver cannot correctly decode packets
  RSSI values reported by chipset do not correspond to actual power level of received packet, but proportional
Notes: (Blue)
PER = packet error rate
RSSI = received signal strength indication

## Slide 24: Operational Range
Setup
  SX1276 LoRa development kit with power amplifier as RF source
  Transmitting 30 dBm signals in 6 dBi patch antenna at 915 MHz
  Backscatter device to transmit LoRa packets at offset 3 MHz, SF=12, BW=31.25 kHz, (8,4) hamming code (3-byte payload, 2-byte CRC)
Two deployment scenarios
Notes: Source transmitting at max power permitted by FCC on 900MHz ISM (instructional, scientific, medical) band

## Slide 25: Applications: Whole-Home Sensing
Previously: limited range and coverage preclude whole-home sensing
LoRa backscattering deployment: 4,800 ft2 three-story house (Δf = 1 MHz)
Backscattering device moved through house in 6x6-ft. grid
Conclusion: coverage is equivalent to typical wireless coverage; sufficient for smarthome IoT devices
Notes: (Blue)
RSSI = received signal strength indication

## Slide 26: Applications: Office Sensing
LoRa backscattering deployment: 13,024 ft2 office with 41 rooms (Δf = 3 MHz)
Backscattering device moved through office in 26x26-ft. grid; source and receiver have sheet-rock, metal, insulation, and offices between them
Conclusion: able to achieve wide-area backscatter coverage in significant multi-path environments
Notes: (Blue)
RSSI = received signal strength indication

## Slide 27: Applications: Precision Agriculture
Deployed on one-acre (~43560 ft2) farm
RF source and receiver on opposite sides
Farm divided into 45ft x 45ft grids
Backscatter device w/ 1MHz offset placed at ground level, between plants and bushes
RSSI measured across 20 locations at center of the grids
Median RSSI = -137 dBm, minimum RSSI = -143 dBm
Conclusion: reliable backscatter communication across a one-acre farm with only one transmitter and receiver
Notes: CDF = cumulative distribution function (remember stats)

## Slide 28: Applications: Smart Contact Lens
Can measure various health indicators (glucose, sodium, cholesterol) in tears
IC not currently possible to place in lens
1 cm diameter loop of 30 AWG wire between two contact lenses
Deployed in 104ft x 32ft atrium with RF source and receiver at opposite ends of the room
Driven by FPGA PoC and sends LoRa packets at 1MHz offset
RSSI measured at center of 12ft x 10ft grids in the room
Conclusion: smart contact lens can communicate via CSS backscatter at farther distances than prior approaches

## Slide 29: Applications: Epidermal Patch Sensor
Measure temperature, sweat, ECG, and other vitals in real time
Sticker RFID antenna (Alien’s Squiggle inlay) connected to FPGA PoC driver
Utilize cheap RFID tags with LoRa backscatter system to create cheap patch sensors
RF transmitter and receiver at opposite ends of 3,328 ft2 atrium
Measuring RSSI of 1MHz offset backscatter signals just as the lens
Conclusion: patch sensor provides reliable connectivity with RSSI greater than -132 dBm
Notes: ECG = electrocardiogram

## Slide 30: Motivation Design Hardware Implementation Results Conclusion References Challenges & Future Work

## Slide 31: Conclusion
LoRa is the first wireless system that operates at km distances while consuming less than 10 µW
Inexpensive, flexible form factor connectivity solutions which can be integrated into everyday objects
Feasible for wide-area deployment: whole-home coverage, precision agriculture, long-range medical implants, and more
Notes: (Blue)

## Slide 32: Motivation Design Hardware Implementation Results References Challenges & Future Work

## Slide 33
Achieving higher data rates
  Currently limited by LoRa
  Use multiple frequency bands or multiple antenna designs?
LoRa-independent design
  Reliance on CSS modulation suggests key innovation is independent of LoRa
Networking high volumes of devices
  Currently limited by TDMA’s upper bound on throughput
Other power sources
  RF power harvesting?
Notes: (Blue)

## Slide 34: Questions?

## Slide 35
https://github.com/PrateekSinghRajput/Post-Graduate-Project-Details-2025
Receiver
NODE 1
NODE 2